## Slide 1
Active Vibration Control of an ASML Measurement Plate
Phase I: Positive Position Feedback with Dual Piezo Patches Phase II: Direct Velocity Feedback with MEMS Accelerometer
Isaak Bouwmeester | ASML Internship | June 2026

## Slide 2
Floor vibrations at the plate's first bending mode degrade wafer positioning accuracy
Motivation
Isaak Bouwmeester | ASML Internship | June 2026
2/18
ASML measurement plate: ~1000x1000 mm aluminium, ~100 mm thick
First bending mode at ~160 Hz (COMSOL); resonance amplifies floor vibrations
Positioning errors at wafer reduce lithography resolution
Goal: suppress the dominant bending mode using active vibration control (AVC)
Approach: piezoelectric patch actuator in closed-loop feedback
Two phases: Phase I - PPF with dual DuraAct patches (Patch 2 actuator + Patch 3 sensor) Phase II - DVF with Patch 2 actuator + MEMS accelerometer (IMU)
Physical Setup
Plate: Al, 1x1 m, 100 mm thick, STL import in COMSOL
Actuator: PI Ceramic P-876.A12 DuraAct (d31 mode)
3-layer: polymer / PIC255 ceramic / polymer
Mounting: Domain Spring Foundation, f_mount ~ 1.7 Hz
BC: elastic isolation (NOT fixed constraint)

## Slide 3
The plate has four flexible bending modes between 87 and 226 Hz; mode 3 at 161 Hz is the DVF target
COMSOL Model
Isaak Bouwmeester | ASML Internship | June 2026
3/18
Mode group
Freq. (Hz)
Description
DVF phase at peak
Spring rigid-body (x6)
1.66-1.68
Translation + rotation on foam mount
N/A
Flexible mode 1
86.51
First bending (actuator placed here)
+51 to +140 deg - distorted
Flexible mode 2
127.78
Second bending
~-90 deg
Flexible mode 3
160.90
Third bending - DVF target
-90 deg - clean
Flexible mode 4
225.56
Fourth bending
~-90 deg
Key: Mode 3 at 161 Hz shows a clean -90 deg phase at the |H22| peak. Mode 1 at 87 Hz has feedthrough-distorted phase (+51 to +140 deg) -- simple DVF cannot reliably suppress it.

## Slide 4
The DuraAct P-876.A12 patch uses d31 bending; three COMSOL material overrides are required
Actuator
Isaak Bouwmeester | ASML Internship | June 2026
4/18
DuraAct layer stack (d31 bending mode, no rotation needed):
  Bottom polymer: 61x35 mm, 0.15 mm thick (E = 5 GPa)
  PIC255 ceramic: 50x30 mm, 0.20 mm thick (active layer)
  Top polymer: 61x35 mm, 0.15 mm thick
Electric field applied through ceramic thickness (z-axis = poling direction)
Va = 1 V on top PIC255 face, Ground on bottom PIC255 face
CRITICAL: COMSOL PIC255 defaults are wrong. Always override: d31 = d32 = -260 pm/V (COMSOL default: -18.5e-11 C/N) epsR_T33 = 1355 (COMSOL default: 1832) Ceramic thickness = 0.20 mm
Patch cross-section (not to scale)
Top polymer 0.15 mm
PIC255 ceramic 0.20 mm
Bottom polymer 0.15 mm
Plate (Al) 100 mm

## Slide 5
Part I Positive Position Feedback with Dual Piezo Patches

## Slide 6
Phase I bonds a second DuraAct patch as an open-circuit voltage sensor for PPF feedback
Phase I Setup
Isaak Bouwmeester | ASML Internship | June 2026
6/18
Patch 3 (sensor): identical DuraAct layup, offset 65 mm in x from Patch 2
Open-circuit condition: Floating Potential on both ceramic faces (top + bottom)
  Do NOT add Ground to either face -- that fixes V = 0 and corrupts Vs
Sensor output: Vs = open-circuit piezo voltage [V/V]
COMSOL model: 7 domains (plate + 3 Patch-2 layers + 3 Patch-3 layers)
Boundary condition: Fixed Constraint on 4 bottom perimeter edge lines
  Geometric entity level must be set to Edge, not Boundary
COMSOL domain layout
Plate (aluminium)
Patch 2 - top polymer
Patch 2 - PIC255 ceramic
Patch 2 - bottom polymer
Patch 3 - top polymer
Patch 3 - PIC255 ceramic
Patch 3 - bottom polymer

## Slide 7
PPF is unconditionally stable because the collocated piezo phase is always within (-90 deg, +90 deg)
PPF Theory
Isaak Bouwmeester | ASML Internship | June 2026
7/18
Plant: H22(s) = H0 * wn^2 / (s^2 + 2*zeta*wn*s + wn^2)
Phase of H22 at resonance: -90 deg (collocated piezo pair)
PPF controller (Baken 2025):
  K_PPF(s) = (1/H0) * g * wf^2 / (s^2 + 2*zf*wf*s + wf^2)
  wf = wn, g = 0.3, zf = 0.3 (Baken values)
Phase accumulation at resonance:
  H22: displacement to Vs = -90 deg
  K_PPF filter: Vs to Va = -90 deg
  Total: -180 deg from displacement = opposing velocity = DAMPING
PPF block diagram:
+ +
d_dis ->
Va
H22
-> Vs ->
K_PPF
(feedback: positive +)
[d_dis] -> (+) -> H22 -> [Vs] -> ^ | | K_PPF <----|
Stability: phase of H22 bounded in (-180 deg, 0 deg). PPF filter adds (-180 deg, 0 deg). Sum never encircles -1. -> Unconditionally stable.

## Slide 8
PPF predicts 22.6 dB suppression at f1 = 214 Hz with g = 0.3 -- matching Baken 2025
PPF Results
Isaak Bouwmeester | ASML Internship | June 2026
8/18
Closed-loop tip displacement (MIMO formula):
  T11 = H11 - H12 * [K_PPF / (1 - H22*K_PPF)] * H21
MATLAB implementation:
  T = feedback(HOLc, K_ppf, 2, 2, +1) (positive feedback, channel 2)
Tuning: g = 0.3, zeta_f = 0.3 (Baken 2025 values)
Predicted suppression at f1 = 214 Hz:
  Delta_H22 = -22.6 dB
  Baken 2025 result: -22.8 dB (sandwich beam, same g/zeta_f)
Discretisation: Tustin method, fs = 10 kHz
  Kd = c2d(K_ppf, 1e-4, tustin)
Comparison: this project vs Baken 2025
Parameter
This project
Baken 2025
Structure
Al plate 1x1 m
Sandwich beam 0.4 m
Eigenfreq f1
214 Hz
29.5 Hz
PPF gain g
0.3
0.3
PPF damp. zf
0.3
0.3
Suppression
-22.6 dB
-22.8 dB
H22 at DC (H0)
~0.22 V/V (est.)
read from FRD

## Slide 9
Part II Direct Velocity Feedback with MEMS Accelerometer

## Slide 10
COMSOL's solid.accZ uses +omega^2 (not -omega^2), shifting the phase 180 deg vs a real accelerometer
Phase Convention
Isaak Bouwmeester | ASML Internship | June 2026
10/18
Physical acceleration: a = (j*omega)^2 * x = -omega^2 * x
  Phase = +180 deg relative to displacement
COMSOL (solid.accZ): derived from inertia term (+omega^2 * M * U)
  solid.accZ = +omega^2 * w = -a_physical
Consequence: 180 deg phase offset vs Falangas 1994 and all papers using real accelerometers
Freq. region
solid.accZ phase
Physical accel. phase
Below resonance (DC)
0 deg
+180 deg
At resonance w1
-90 deg
-270 deg (+90 deg)
Above resonance
-180 deg
-360 deg (0 deg)
Confirmed from H22_accel.txt data: at 1 Hz, H22 is positive real (0 deg) -- COMSOL convention. Resonance at ~157 Hz, phase crosses -90 deg there.

## Slide 11
PPF and IRC both fail with an acceleration sensor; DVF is conditionally stable and applicable
Controller Selection
Isaak Bouwmeester | ASML Internship | June 2026
11/18
Strategy
Stability condition
H22 phase at resonance
Verdict
PPF
Angle H22 in (-90, +90) deg
-90 deg -- on boundary
REJECTED: unsafe
IRC
Im[H22] <= 0 for all w (Negative Imaginary)
NI holds only for disp./ strain sensors, not accel.
REJECTED: proof invalid
DVF
Nyquist: g*H22_vel does not encircle -1
H22_vel real and positive at resonance
SELECTED: conditionally stable
DVF conditional stability (Gatti 2007): patch actuator applies a distributed bending moment, not a point force -- Balas (1979) unconditional stability does NOT apply. Maximum stable gain g_max must be found from the Nyquist plot.

## Slide 12
DVF uses +g sign (not -g) with solid.accZ data -- the literature sign assumes physical acceleration
DVF Sign Convention
Isaak Bouwmeester | ASML Internship | June 2026
12/18
DVF controller (Falangas 1994 formulation):
  K_DVF(s) = +g * S / (s + S), S = 5 rad/s (~0.8 Hz cutoff)
  Feedback: NEGATIVE (summing junction carries minus sign)
Why +g (not -g from paper):
  Falangas writes K = -g*S/(s+S) assuming a = -omega^2 * x (physical)
  solid.accZ uses a = +omega^2 * x (COMSOL convention)
  Feeding solid.accZ into -g flips damping -> anti-damping
  -> use +g to restore genuine velocity damping
Symptom of wrong sign:
  Suppression dB is POSITIVE and grows with gain (amplification, not suppression)
  Nyquist gain margin lands exactly on f1 (should be a different mode)
DVF block diagram:
+ -
d_dis ->
Va
H22
-> a_imu ->
+g*S/(s+S)
[d_dis] -> (+/-) -> H22 -> [a_imu] -> ^ | | +g*S/(s+S) <---|
Numerics: at resonance H22*K = (-jM)(j*gL) = +MgL > 0 Denominator = 1 + MgL > 1 -> T21 = H21/(1+MgL) < H21 -> genuine suppression

## Slide 13
Only Domain Spring Foundation is consistent between Study 1 (Va) and Study 2 (base) for a correct MIMO matrix
Boundary Conditions
Isaak Bouwmeester | ASML Internship | June 2026
13/18
BC approach
Study 1 (H22, H12)
Study 2 (H11, H21)
Verdict
Fixed Constraint (4 bottom edges)
Works: f1 ~214 Hz
Over-constrains plate: f1 jumps to ~6500 Hz
Phase I only
Boundary Spring Foundation
Works
FAILS: contradicts Base Excitation node -> flat H11
REJECTED
Rigid Motion Suppression (RMS)
Works
Different eigenmodes than Study 1 -> inconsistent MIMO
REJECTED
Domain Spring Foundation + Base Excitation node
Works: 6 spring modes at ~1.7 Hz
Correct: H21 ~ 1 at DC, resonances at correct freq.
SELECTED: Phase II

## Slide 14
DVF predicts 10-15 dB suppression at 161 Hz, consistent with Falangas 1994's 10.5 dB benchmark
DVF Results
Isaak Bouwmeester | ASML Internship | June 2026
14/18
Closed-loop transmissibility (primary metric: IMU corner):
  T21 = H21 / (1 + H22 * K_DVF)
Controller: K_DVF = +g * 5/(s+5), g = 0.30 * g_max
g_max from Nyquist: g_max = 1 / max(-Re[H22 * S/(jw+S)])
Operating gain: g = 30% of g_max (10 dB stability margin)
Predicted suppression: Delta_T21 ~ -10 to -15 dB at f1 = 161 Hz
Falangas 1994 benchmark: -10.5 dB (rate feedback on flat plate + PZT)
Gain sweep at 10%, 20%, 30%, 50%, 70%, 80% of g_max:
  Available in dvf_main.m (Figure 5 output)
Actuator voltage check: Va_peak = g * K_norm * H21(f1) * a_rms
  Limit: 400 V (P-876.A12 max). Both stability and voltage limit checked.
Reference figure to compare: Falangas 1994, Figure 7 -- closed-loop transmissibility of flat aluminium plate with PZT patches and rate feedback. Target: indent at f1 ~10 dB deep.
Not yet available (needs COMSOL re-export):
  T11 = H11 + H12 * K / (1 + H22*K) * H21 (tip transmissibility)
    -> Re-export H11 and H12 at IMU corner from Study 2 / Study 1

## Slide 15
Conclusions: DVF with correct sign is the viable controller; H11/H12 re-export completes the MIMO validation
Conclusions
Isaak Bouwmeester | ASML Internship | June 2026
15/18
Phase I -- PPF with dual DuraAct patches:
  Unconditionally stable due to collocated piezo phase bound
  -22.6 dB predicted suppression at 214 Hz (matches Baken 2025: -22.8 dB)
Phase II -- DVF with MEMS accelerometer:
  PPF and IRC both inapplicable with acceleration sensor
  DVF with +g (not -g) restores genuine velocity damping with solid.accZ data
  -10 to -15 dB suppression predicted at 161 Hz (target mode)
Critical model decisions:
  Domain Spring Foundation: only BC consistent between Study 1 and Study 2
  161 Hz is the reliable DVF target; 87 Hz has feedthrough-distorted phase
  PIC255 d31 and epsR must be overridden from COMSOL defaults
Remaining work: re-export H11 and H12 at IMU corner to complete T11 calculation

## Slide 16
References
Isaak Bouwmeester | ASML Internship | June 2026
16/18
[1] E.T. Falangas, J.A. Dworak, S. Koshigoe, "Controlling plate vibrations using PZT actuators," IEEE Control Syst. Mag., 14(4):34-41, 1994.
[2] G. Gatti, M.J. Brennan, P. Gardonio, "Active damping of a beam using a collocated accelerometer and PZT patch," J. Sound Vib., 303:798-813, 2007.
[3] S.S. Aphale, A.J. Fleming, S.O.R. Moheimani, "Integral resonant control of collocated smart structures," Smart Mater. Struct., 16(2):439-446, 2007.
[4] M.J. Balas, "Direct velocity feedback control of large space structures," J. Guidance Control, 2(3):252-253, 1979.
[5] C.J. Goh and T.K. Caughey, "On the stability problem caused by finite actuator dynamics," Int. J. Control, 41(3):787-802, 1985.
[6] M. Baken, V. Gupta, B. Jansen, S.H. HosseinNia, "Harnessing PZT shear actuators for vibration control in sandwich beams," arXiv:2506.21713v1, 2025.